## Slide 1
BNPB DISASTER INTELLIGENCE PLATFORM
Our Scope & Solution Overview
Aligned with BNPB High-Level System Diagram
DATA SOURCES
Rainfall Radar
River Water Level
Landslide Sensors
CCTV / Cameras
UAV / Drones
Satellite Imagery
Social Media
News / RSS
DATA INGESTION &
INTEGRATION
Real-time Stream
Ingestion (Kafka)
Data Validation &
Quality Control
Master Data
Management
Data Lake
(Raw & Processed)
CORE INTELLIGENT PLATFORM ◀ OUR SCOPE
① EWS LAYER
Monitor hazard in real-time
• Hydrology & hydraulic
model for Flood
(HEC-HMS / HEC-RAS)
• Geotechnical model
for Landslide
(TRIGRS / FLO-2D)
• ML-driven predictive
modeling for alerting
enhancement
Outputs
On-the-fly flood &
landslide detection
② ANALYTICS LAYER
Produce insights for disaster area
• Risk assessment &
scoring (30 GIS/
hazard models)
• Vulnerability &
exposure analytics
• Disaster scenario
analytics (evacuation,
logistics, funding)
Outputs
Risk level, impact
estimate, action planning
③ DISSEMINATION
Deliver to relevant users
• GenAI-powered
summarization
• BNPB SOP
integration
• Multi-channel alerts
(SMS, Push, Email)
Outputs
Push notifications,
Information summary
USERS
BNPB Officers
(Full Admin)
BPBD Regional
Users
Public
(Read-only)
Third-party
Integrators
BNPB National Multi-Hazard Disaster Monitoring & Decision Support System | Confidential
1 / 4

## Slide 2
USE CASE: FLOOD HAZARD MONITORING & EARLY WARNING
HEC-HMS / HEC-RAS Physical Modeling + AI/ML Prediction
EWS Layer
EWS Layer ①
DATA INPUTS
1
River water level sensors
Rainfall gauges (rain intensity)
Satellite imagery (LAPAN)
UAV/drone terrain scans
DEM / elevation data
Upstream dam status
▶
PHYSICAL MODELING
2
HEC-HMS: Rainfall-Runoff
& Watershed Hydrology
HEC-RAS: River Hydraulics
& Inundation Modeling
Water discharge & flow velocity
calculation
Flood depth simulation
across river basin
▶
AI / ML ENHANCEMENT
3
LSTM Neural Networks
for flood forecasting
Random Forest flood
susceptibility mapping
MCDM-AHP risk
assessment scoring
Flash flood predictive
modeling (real-time)
▶
OUTPUTS & ALERTS
4
Flood extent & inundation map
Population & infrastructure
exposure index
Evacuation safe zone analysis
Early warning triggers
(SMS, Push, Dashboard)
Scientific Basis:
Kratzert et al. (2018) – LSTM for Rainfall-Runoff | USACE HEC-HMS/HEC-RAS Technical Reference | Tehrany et al. (2015) – Random Forest Flood Susceptibility | Kazakis et al. (2015) – MCDM-AHP Flood Risk
BNPB National Multi-Hazard Disaster Monitoring & Decision Support System | Confidential
2 / 4

## Slide 3
USE CASE: LANDSLIDE HAZARD MONITORING & EARLY WARNING
TRIGRS / FLO-2D Geotechnical Modeling + AI/ML Susceptibility Analysis
EWS Layer ①
DATA INPUTS
1
SRTM DEM elevation data
SMAP Soil moisture data
GPM IMERG rainfall data
Sentinel-1 SAR imagery
Slope & geological maps
IoT landslide sensors
▶
GEOTECHNICAL MODELING
2
TRIGRS: Transient rainfall
infiltration & grid-based
regional slope stability
FLO-2D: Debris flow
& hyperconcentrated
flow simulation
Rainfall threshold
analysis for triggering
Slope stability index
mapping
▶
AI / ML ENHANCEMENT
3
SVM Landslide
susceptibility mapping
XGBoost/Gradient Boosting
slope classification
SAR Interferometry
(InSAR) displacement
detection
Rainfall-threshold
prediction model
▶
OUTPUTS & ALERTS
4
Landslide susceptibility
zone map
Displacement & ground
deformation detection
At-risk population &
infrastructure exposure
Early warning triggers
& evacuation routing
⚠ Data Requirement Note:
TRIGRS & FLO-2D require site-specific geotechnical data (soil properties, infiltration rates, flow rheology). BNPB is requested to provide or facilitate access to these datasets. Macro-scale AI/ML analysis (SVM, XGBoost, InSAR) will operate on satellite datasets available from the outset.
BNPB National Multi-Hazard Disaster Monitoring & Decision Support System | Confidential
3 / 4

## Slide 4
DATA FLOW (COMMON) — SOLUTION PROCESS IN A NUTSHELL
AI model explained for each solution — detailed per section
Applies to: Flood | Landslide | Wildfire
High-res Satellite
Imagery for HIGH-RISK AoIs
🛰 LAPAN | Sentinel-1 SAR
MODIS | VIIRS Thermal
Geospatial
Characteristics Data
1) Waterbodies
2) Road Network
3) TWI (Topographic
Wetness Index)
4) Elevation (DEM)
5) Vegetation
6) Impervious Surface
7) Landslide/Fire Risk
Index
8) Building Footprints
Ancillary Datasets
+ Ground Truth
INPUT DATA
▶
Data Pre-Processing Engine
Collection, Storage, Indexing, Transformation & Retrieval
Data Normalization
Standardize formats, CRS
projection, units
Initial Stats &
Computations
Feature extraction,
statistical summaries
Data Enrichment
Merge geospatial layers,
enrich with metadata
Data Labeling
(Auto/Semi-Auto)
Ground truth matching,
ML-ready label generation
▶
Post-Processing Engine
Risk Score Adjustment, Human SME in the loop
Classification /
Reclassification
of Risk Score
Business
Rule Engine
Human SME Override & Validation
Human SME Override
& Expert Validation
▼
AI Model Pipeline
Input Pipeline
Data ingestion & feature prep
Model Pipeline
Training, validation, inference
Output Pipeline
Results, scoring, maps
AI Model*
Building Footprint + Computer Vision
+ Risk Modeling + Vulnerability & Exposure
▶
▶
OUTPUTS & VISUALIZATION
Web-App Dashboard
Maps, heatmaps, hazard layers,
vulnerable hotspots
Hazard Risk Maps
Flood/Landslide/Wildfire extent,
exposure & severity index
Analytics Reports
Pre/during/post disaster
summaries & comparisons
Alert System
Automated SMS, push & email
with BNPB SOP actions
▶
END USERS
Disaster
Mitigation Staff
Interactive advisory
for on-ground action
BNPB Officers
Full system access,
configuration
BPBD Regional
Scoped regional
dashboards & alerts
Public
Read-only hazard maps
& early warnings
* This is a tentative architecture. Subject to availability of data and requirement gathering phase.
BNPB National Multi-Hazard Disaster Monitoring & Decision Support System | Confidential
4 / 4