## Slide 1
Processing Latency & System SLAs (End-to-End)
From rainfall observation / sensor trigger to alert delivery at the decision-maker's device
FLOOD MODELLING & EARLY ACTION
From rainfall observed to alert delivered
LANDSLIDE MODELLING & EARLY ACTION
From critical rainfall/sensor trigger to BPBD alert delivery
Workflow Stage | KPI Target | Hard Ceiling | Measurement Metric
1. Sensor Ingest & QC | ≤ 2 min | 3 min | Time from IoT node transmission to stream ingest & Hampel filtering completion.
2. Rainfall Fusion | ≤ 4 min | 6 min | Merge sensors and BMKG gauges with IMERG/GSMaP satellite data via residual kriging.
3. Hydrological Run | ≤ 3 min | 5 min | WFLOW_sbm generates forecast discharge at all sub-basin outlets.
4. Threshold Check | ≤ 1 min | 2 min | Compare forecast against return periods (Q₂₅ᵧᵣ) and formulate alert.
5. Alert Dissemination | ≤ 2 min | 3 min | Push API payload to InaRISK, SMS broadcast, and BPBD dashboards.
End-to-End Total | ≤ 15 min | 20 min | Total time from rainfall observed to alert delivered.
COMPLIANCE: 95% of forecast cycles must complete within the 15-minute target; 99% must complete within the 20-minute hard ceiling.
Workflow Stage | KPI Target | Hard Ceiling | Tech Stack / Methodology
1. Sensor Ingest & QC | ≤ 1 min | 2 min | Ingestion of IoT landslide sensors (tiltmeters/extensometers) & SMAP soil moisture data.
2. Dynamic Susceptibility | ≤ 2 min | 4 min | Execution of XGBoost classification / SVM models based on new GPM IMERG rainfall data inputs.
3. Runout Modeling | ≤ 5 min | 8 min | Dynamic Debris & Mudflow Routing (e.g., RAMMS / Flow-R).
4. Exposure & Alerting | ≤ 2 min | 3 min | Intersect hazards with population density/infrastructure to generate Pre-Disaster warning information.
End-to-End SLA | ≤ 10 min | 17 min | Total time from critical rainfall/sensor trigger to BPBD alert delivery.
ALERT DELIVERY: Total time from critical rainfall/sensor trigger to BPBD Pusdalops alert delivery.