## Slide 1
AXIS P1488-LE Bullet Camera — Sensor Specification & EAS Integration
Visual / Optical sensor for real-time flood and landslide early action system monitoring
SENSOR SPECIFICATIONS
AXIS P1488-LE · 8MP Fully-Featured AI-Powered Surveillance
Parameter
Details
Sensor Name
AXIS P1488-LE Bullet Camera
Sensor Type
Visual / Optical Sensor — 8MP fully-featured AI-powered surveillance
Frequency of Capture
Continuous real-time video streaming at up to 50/60 frames per second
Resolution & Output
High-resolution 4K / 8MP video in any light condition
Object Analytics
Preinstalled AXIS Object Analytics — detects humans & vehicles in specific areas, tracks line crossing, monitors spatial behavior
AI Classification
Detect, classify, and count objects in real-time; area intrusion, loitering detection
Local Storage
AXIS Surveillance Card 128GB (high-endurance SD) — failover recording inside camera
Recording Server
AXIS S1296 Rack Recording Server — 96TB or 192TB high-capacity video storage
VMS Software
AXIS Camera Station Pro — view, manage, and configure access control for all feeds
KEY THRESHOLDS
Flood Trigger:
Water level ≥ bankfull − 30 cm freeboard
Vehicle Access Limit:
Flood depth > 0.3 m restricts emergency vehicle access
Human Stability:
Debris flow depth > 0.5 m and flow velocity > 0.3 m/s
EAS MODEL APPLICATIONS
Applicable geospatial / physical models
FLOOD MODELLING & EARLY ACTION
Stage 2 — River Hydraulics
Visual verifier for Gridded WSE output. Confirms trigger: water level ≥ bankfull − 30 cm freeboard.
Stage 4 — Flood Depth & Impact
Validates flood extent + inundation map. AI analytics confirm Depth > 0.3 m restricts emergency vehicle access.
LANDSLIDE MODELLING & EARLY ACTION
Parameter 4 — Debris & Mudflow Routing
Validates RAMMS/FLO-2D output (mudflow footprint: max depth + impact force). Visual feed confirms if debris flow breaches human stability limits: Flow depth > 0.5 m and Flow velocity > 0.3 m/s.
ALERT DELIVERY: Continuous real-time video feed enables immediate visual verification of model outputs for BPBD alert dispatch.
SUPPORTING INFRASTRUCTURE
⚡ Power
SUPBLP 24100 (24V 100Ah LFP Battery), SUPSM-390 (390W Solar), SGPE-300 Inverter, 40×30×15 cm Steel Panel Box
📡 Network
Teltonika RUT951 PoE+ (4G LTE industrial router — powers & connects camera via PoE+)
AXIS P1488-LE | Real-Time Visual Verification | Flood & Landslide EAS Integration | Continuous 50/60 FPS · 8MP · AI Object Analytics