## Slide 1
Non-Visual Sensor Suite — Specification & EAS Integration
Precipitation · Ultrasonic Level · Ground Deformation Radar — Flood & Landslide Early Action System
① MACSENSOR R66S — Precipitation / Tipping Bucket Rain Gauge
MSR103 DTU transmits via cellular · Powered by 24V 100Ah LFP Battery + 390W Solar + PSW 300W Inverter
Sensor Name
MACSENSOR R66S
Sensor Type
Precipitation / Tipping Bucket Rain Gauge
Frequency of Capture
Continuous analog collection — event-triggered per 0.2 mm (default) or 0.5 mm tip
Rain Intensity Range
0 – 4 mm/min
Resolution
0.2 mm (default) or 0.5 mm per tip
Information Provided
Quantifies rainfall depth & intensity in real-time; feeds I-D threshold models
② MACSENSOR UL103 — Ultrasonic Level / Distance Sensor
Non-contact measurement · Adjustable response 0.5 s – 10 s via software or Modbus
Sensor Name
MACSENSOR UL103
Sensor Type
Ultrasonic Level / Distance Sensor
Frequency of Capture
Adjustable: 0.5 s to 10 s response time (software / Modbus configurable)
Measurement Range
2.5 m · 5 m · 10 m · 15 m (model dependent)
Accuracy
0.5% F.S. (typical) · 0.25% F.S. (high accuracy mode)
Information Provided
Non-contact water surface elevation & depth monitoring for bankfull and access thresholds
③ MAS Deformation Radar — Models MAS-R1S · R2S · R5
Ground-based Interferometric Radar (D-InSAR) · Sub-millimeter slope deformation measurement
Sensor Name
MAS Deformation Radar (MAS-R1S, R2S, R5)
Sensor Type
Ground-based Interferometric Radar (D-InSAR)
Frequency of Capture
MAS-R1S: 6 s update rate · MAS-R2S & R5: better than 1 update/min
Accuracy
0.1 mm deformation measurement accuracy (sub-millimeter)
Technology
Differential Interferometric Synthetic Aperture Radar (D-InSAR)
Information Provided
Surface deformation velocity & displacement — physical ground-truth for slope stability
EAS MODEL APPLICATIONS
Applicable geospatial / physical models per sensor
FLOOD MODELLING & EARLY ACTION
R66S — Stage 1: Rainfall-Runoff & Watershed Hydrology
Directly measures the Rainfall I-D threshold and provides raw data to calculate how much rain reaches the river. 0–4 mm/min intensity feeds hydrological models.
UL103 — Stage 2: River Hydraulics & Inundation
Measures water surface elevation to trigger: Channel capacity breach — water level ≥ bankfull − 30 cm freeboard.
UL103 — Stage 4: Flood Depth & Impact Footprint
Continuously monitors depth to verify if it breaches Depth > 0.3 m, which restricts emergency vehicle access.
LANDSLIDE MODELLING & EARLY ACTION
Radar — Parameter 1 & 2: Slope Stability
Sub-millimeter (0.1 mm) accuracy provides physical ground-truth to Transient FS (Factor of Safety) rasters — shows exactly how much slope is failing during a storm before debris flow begins.
R66S — Parameter 3: Rainfall Threshold for Triggering
Acts as gauge telemetry feeding Empirical Intensity-Duration (I-D) Threshold Models. 0–4 mm/min capture matches data needed for the power-law equation I = α · D^(−β).
KEY THRESHOLDS
Flood Trigger:
Water level ≥ bankfull − 30 cm freeboard (UL103)
Vehicle Access:
Depth > 0.3 m restricts emergency vehicle access (UL103)
I-D Rainfall:
Intensity I = α · D^(−β) — 0–4 mm/min range (R66S)
Slope Stability:
FS raster ground-truth at 0.1 mm accuracy (Radar)
SUPPORTING INFRASTRUCTURE
📡 MSR103 DTU
Industrial IoT wireless terminal — transmits sensor data via cellular network
MACSENSOR R66S | MACSENSOR UL103 | MAS Deformation Radar | Flood & Landslide EAS Integration | Transmitted via MSR103 DTU