## Slide 1
Sensor Inventory & Applicable Physical / Geospatial Models
Field-deployed sensors powering the Flood and Landslide Early Warning workflow
Sensor Name | Sensor Type | Frequency of Data Capture | Sensor Details | Applicable Physical / Geospatial Models
MACSENSOR R66S | Precipitation / Tipping Bucket Rain Gauge. | Event-based (outputs a pulse per tip). Supports a rain intensity range of 0–4mm/min (max 8 mm/min). | Accumulated precipitation/rainfall amount in millimeters (mm). Resolution of either 0.2mm or 0.5mm per tip. | Hydrological routing models (e.g., HEC-HMS), Catchment runoff models, Meteorological and flood forecasting models.
MACSENSOR UL103 | Water Level / Ultrasonic Distance Sensor. | Adjustable response time from 0.5s to 10s via software or Modbus commands. (Default is 0.5s for 2.5m/5m ranges; 1s for 10m; 2s for 15m). | Non-contact liquid level or distance measurement (Ranges: 2.5m, 5m, 10m, 15m). Accuracy up to 0.25% F.S. to 0.5% F.S. | Hydrodynamic routing (e.g., HEC-RAS), Flood inundation mapping, Reservoir/Tank volume tracking models.
MAS Deformation Radar (Models MAS-R1S, R2S, R5) | Displacement / Ground-based Interferometric Radar. | MAS-R1S: Deformation update rate of 6 seconds. MAS-R2S & R5: Update rate of better than 1 time/minute for a 180° scan. | Sub-millimeter structural and slope deformation measurement with 0.1 mm accuracy. Provides 3D deformation cloud diagrams fused with topographic maps. | Geotechnical stability models, Landslide/Slope failure prediction models, Limit Equilibrium Method (LEM), Digital Elevation Models (DEM).
AXIS P1488-LE | Visual / Optical Sensor (AI-powered surveillance). | Continuous video capture up to 50/60 frames per second. Analytics trigger events instantly based on configured scenarios. | 8 MP video imaging. Via AXIS Object Analytics, it provides AI-based detection, classification (humans, vehicles, bikes), spatial occupancy, and crossline counting. | Traffic and pedestrian flow modeling, Spatial occupancy models, Security and surveillance event mapping.
Sensitivity Label: General